## Slide 1: Capacitated Design: Part II
B
Dr. Greg Bernstein
Grotto Networking
www.grotto-networking.com

## Slide 2: Outline
Demand splitting across Paths
  How does this come about? When is it allowed?
Limited Demand Split (Section 4.2.3)
  Link-Path, Node-Link
  No splitting
Technologies for Inverse Multiplexing
  MLPP, VCAT, But not LAG
Other Constraints
  Forbidden links or paths (Example 4.1 page 111)
  Bi-directional assignment in Node-Link formulation
Quick Feasibility Checks
  Maximum flow between two nodes
  Widest Path between two nodes

## Slide 3: Demand Splitting
What is it?
  It occurs during optimization when flow for a demand is split amongst multiple paths.
Does this represent a valid solution?
  It depends on the technologies available.

## Slide 4: Splitting Example
Capacitated Allocation Problem
  Node-Link Formulation with 18 directed links
  5 Demands
  Links all have same weight and capacity
Demands:
Links:

## Slide 5: Splitting Example (cont)
  Demand <N1, N6> split into 3 paths
  Demand <N3, N5> split into 2 paths

## Slide 6: Splitting Example (cont)
Why splitting?
  Demands <N1,N6>, <N2,N0>, and <N0,N3> might all want to use similar shortest paths
    In this optimal solution link loads are: (u'N0', u'N6'): 40.0, (u'N1', u'N0'): 40.0 (saturated)
    Seems like splitting is needed for optimality
  What about demand <N3, N5>:31 ?
    Link loads (N3,N6): 40, (N6,N5): 23; (N3, N4): 17, (N4, N5): 17
    Looks like room to put the whole demand on the {N3, N4, N5} path.
    Splitting because paths had equal weight

## Slide 7: Splitting Example (cont)
Directed Network, Directed Demands
  Path chosen not necessarily symmetric!
  Technologies such as SONET, SDH, and G.709 require bi-directional symmetry of paths
Symmetric
Not Symmetric

## Slide 8: What can be done?
The Usual Answer
  Add some kind of constraint…
Modified Link-Path Formulation I
  Path flows (we’ll have a variable per demand and per path)
  New Binary variables for each path flows (1 indicates the path is used, 0 not used)
  Objective: minimize
    is the cost of link e
    indicator if link e is in path d,p

## Slide 9: Modified Link Path Formulation I
Constraints
  Demand satisfaction & “all or nothing”:
  for and
  for
Link Capacity
  for

## Slide 10: That was easy?
Bad News
  The single path flow allocation problem is NP-Complete
Link Path Formulation II (better)
  Don’t really need
  Objective minimize:
  for (what does this do?)
  Link capacities:

## Slide 11: Example: Link-Path (Splitting)
Demands: <N1,N6>:24, <N0", "N3>:: 25, <N2, N3>: 29, <N0", N2>: 16, <N3, N5>: 31
Candidate paths: ["N2", "N3"], ["N2", "N1", "N0", "N6", "N3"], ["N0", "N6", "N3"], ["N0", "N1", "N2", "N3"], ["N1", "N0", "N6"], ["N1", "N2", "N3", "N6"], ["N0", "N1", "N2"], ["N0", "N6", "N3", "N2"], ["N3", "N4", "N5"], ["N3", "N6", "N5"]
Link Capacity: 40 units all links
Solution:
xDN0_N2P_0 = 16.0
xDN0_N2P_1 = 0.0
xDN0_N3P_0 = 20.5
xDN0_N3P_1 = 4.5
xDN1_N6P_0 = 19.5
xDN1_N6P_1 = 4.5
xDN2_N3P_0 = 29.0
xDN2_N3P_1 = 0.0
xDN3_N5P_0 = 31.0
xDN3_N5P_1 = 0.0

## Slide 12: Single Path Link-Path in Python
Note use of “Binary” variables.
From Solver:
Status: Undefined
xDN0_N2P_0 = 1.0
xDN0_N2P_1 = 0.0
xDN0_N3P_0 = 0.82
xDN0_N3P_1 = 0.18
xDN1_N6P_0 = 0.8125
xDN1_N6P_1 = 0.1875
xDN2_N3P_0 = 1.0
xDN2_N3P_1 = 0.0
xDN3_N5P_0 = 1.0
xDN3_N5P_1 = 0.0

## Slide 13: What Happened?
PuLP returned “undefined”
  Try CBC from command line:
    cbc SPLinkPathEx1Paths2.lp
Problem doesn’t have a solution!!!
  What can we do?
    Change Network (expensive)
    Reduce Demands (loose customers)
    Try more paths

## Slide 14: Single Path Example (cont.)
More Paths: Use three per demand
  <N1,N6>:24, <N0", "N3>:: 25, <N2, N3>: 29, <N0", N2>: 16, <N3, N5>: 31
Status: Optimal
xDN0_N2P_0 = 1.0
xDN0_N3P_0 = 1.0
xDN1_N6P_2 = 1.0
xDN2_N3P_0 = 1.0
xDN3_N5P_0 = 1.0
Actual Paths used:
["N0", "N1", "N2"]
["N0", "N6", "N3"]
["N1", "N0", "N5", "N6"]
["N2", "N3"]
["N3", "N4", "N5"]
Use of 3rd choice path

## Slide 15: Single Path Allocation Node Link Formulation
Constants
  = 1 if link e originates at node v, 0 otherwise
  = 1 if link e terminates at node v, 0 otherwise
  source node of demand d
  sink node of demand d
  volumne of demand d
  unit cost of link e
  capacity of link e
Variables
  binary indicator for flow realizing demand d allocated to link e
Objective
  Minimize
Constraints
  Node balance
  Link capacity
See page 121 of P&M

## Slide 16: SPA Node-Link in Python I

## Slide 17: SPA Node-Link in Python II

## Slide 18: Example SPA Node-Link

## Slide 19: SPA Node-Link Extra Feature
Limiting number of hops per demand path?
  How could we do this…
  How about:
  Where is the hop count limit for each demand.
Example
  Encourage demand <N1, N6> to take a shorter path

## Slide 20: Example Hop Count Limit
This worked, forced other demands to take longer paths!

## Slide 21: Inverse Multiplexing
General Notion
  The breaking of a high speed stream into several smaller streams and their reassembly at the destination
  https://en.wikipedia.org/wiki/Inverse_multiplexing
Virtual Concatenation (SONET, SDH, G.709)
  Included in G.707 and G.709, Link Capacity Adjustment Scheme (LCAS) in G.7042
  G. Bernstein, D. Caviglia, R. Rabbat, and H. Van Helvoort, “VCAT-LCAS in a clamshell,” IEEE Communications Magazine, vol. 44, no. 5, pp. 34–36, May 2006.
  You’ll get to read about this…
Multi-Link PPP (point to point protocol)
  https://en.wikipedia.org/wiki/Point-to-Point_Protocol#Multilink_PPP
  Rather old technology
May be done at “Application Layer”
  How?

## Slide 22: Forbidden Links or Paths
Network Example
  Links to data centers are different from other links. Why?
  Data centers contain lots of switches but we may not want to treat them as switches. Why?
  What happens if we apply k-shortest paths blindly to this network? What about a Node-Link design problem formulation?

## Slide 23: Shortest Paths…
Computing k-shortest paths from DC1 to DC4 as part of a Link-Path formulation, got the path below
Not good, really shouldn’t use DC2 as a “transit” node
How can we avoid this problem?
How can you tell which of the above paths are “bad”?

## Slide 24: Shortest Paths…
Still using k-shortest paths algorithm for paths from DC1 to DC4 I was able to get the paths shown below
How did I do this?
How can we avoid this problem?

## Slide 25: Restrictions on Link Flows
In a Node-Link capacitated allocation problem how can I prevent the flow for the demand <DC2, DC6> from going through DC5? Etc…
Answer:
Add constraints to set the following link flow variables to zero
X_LN4DC5_DDC2DC4 = 0.0
X_LDC5N5_DDC2DC4 = 0.0
Etc…

## Slide 26: Bidirectional Assignment with Node-Link Formulation
Node-Link Formulation
  Works with directed graphs
  Treats all demands as directed too
Some technologies assume bidirectionality
  SONET, SDH, PDH (old E1,T1 hierarchies)
How?
  Must make the network directed but symmetric
  Must make the demands symmetric
  Must force the flows traversing a bidirectional link pair for a bidirectional demand pair to be equal.

## Slide 27: Feasibility Checks
Necessary versus Sufficient conditions
  https://en.wikipedia.org/wiki/Necessity_and_sufficiency
  We would like quick checks of allocation feasibility
  The assertion that Q is necessary for P is colloquially equivalent to "P cannot be true unless Q is true," or "if Q is false then P is false.“ (wikipedia)
What would be a computationally “easy” check for feasibility for a SPA problem?
  For each demand pair check if the capacity of the widest path is less than the demand volume. If it is then the problem is infeasible.

## Slide 28: Feasibility Check for Allocation with Splitting?
Could look at each demand pair and ask if the maximum allowed flow between that pair (alone) is less than the demand. If so then the problem is infeasible.
  But how hard is it computationally to find the maximum flow between to nodes in a network?
  https://en.wikipedia.org/wiki/Max_flow
  Edmonds-Karp (Ford-Fulkerson) algorithm https://en.wikipedia.org/wiki/Edmonds%E2%80%93Karp_algorithm runs in time.
  See also Max-Flow/Min-cut theorem
  Available in NetworkX

## Slide 29: Examples
Widest path v1 to v5 has capacity 14. Why?
Max flow from v1 to v5 is min(28, 25, 46) = 25 by max flow/min cut or Edmonds-Karp
Links