## Slide 1: Topological Network Design: Access Networks
B
Dr. Greg Bernstein
Grotto Networking
www.grotto-networking.com

## Slide 2: Outline
Topological Design Problem Types
  Location and installation costs
Node Placement Problems
  chapter 6 (intro information), 6.1 (but not 6.1.1) access, but not proof of proposition 6.1.
Link Installation Costs
  Book sections 2.7 (pg 65), 6.3 (pg. 230-234)

## Slide 3: Node Placement Problems
Network Access/Edge
  Where to put points of presence (PoPs).
  Where to put core network edge nodes
Servers and Content
  Where to locate web or application servers for a given customer base
  Where to locate content replicas in a CDN

## Slide 4: Access network design problem
Figure out where to install “access nodes” how to connect to “user areas”
Fixed user area locations
Possible access node locations

## Slide 5: Requirements & Costs
  N user regions (areas) all must have network access
    Each region must map to one and only one access node
    The cost of connecting user region i to access node j is
    Why might these vary? How might you set these?
  M possible access node locations
    Each node location, j, has a cost
    Why might these vary?
    Each node location j can support user regions
    Why might these vary?

## Slide 6: Variable Selection
Where to put the nodes?
  Use a binary variable to indicate if a particular access node is used
  if node j is used in the design, 0 otherwise.
How to connect regions to nodes?
  Use a binary variable to indicate if area i is to connect to access node j in the design

## Slide 7: Requirements as Constraints
User region service requirement
  A user region must connect to one and only one node
  for all user regions
Capacity limits of an access node location j
  If a node location is used then the total number of user regions connected to it must be less than its capacity
  for access node

## Slide 8: Objective
Minimize Cost
  Cost of each node location
  Cost of connecting each user region to an access node
Total connectivity cost
Total location cost

## Slide 9: Generating Test Problems
Use geometric distance for connectivity cost between users and nodes.
Generate two types of nodes and place into a graph (n_users, n_nodes)
Give nodes random locations within prescribed limits.
Try different values of node capacity and location costs to see how these influence the problem.

## Slide 10: Python Problem Generator
Example usage:

## Slide 11: Example Network 2
Access node locations modified from purely random

## Slide 12: Example Network 3
Access node locations modified from purely random

## Slide 13: Python MIP Formulation
Problem formulation function:

## Slide 14: Python Formulation Setup
User and access type node lists
  Need these to generate variables
Distances
  Put in a dictionary for generality, but could have directly used the distance() function.

## Slide 15: Python Formulation: Variables & Objective
User-Access link like variables,
Access node use variables
Objective function in terms of link and node costs

## Slide 16: Python Formulation: Constraints
Node capacity constraints
User connectivity constraints
Node capacity
Node a indicator

## Slide 17: Example 1A
K = 6, Cost = 50 per node, Average distance from user to access node 268.8.
Note 8 out of 10 access nodes used. Why aren’t the access nodes being used to capacity?

## Slide 18: Example 1B
K = 6, Cost = 500 per node, Average distance from user to access node 268.8.
Note 5 out of 10 access nodes used. Why are the access nodes running at full capacity?