## Slide 1: Topological Network Design: Link Locations
B
Dr. Greg Bernstein
Grotto Networking
www.grotto-networking.com

## Slide 2: Outline
Network Node Types
  Access vs. transit
Expenses:
  Capital and Operating
Link Placement Problem
  With installation (capital) and operating costs
  Book sections 2.7 (pg 65), 6.3 (pg. 230-234)

## Slide 3: Node Types
Access Nodes
  Originate and terminate traffic demand but do not switch traffic not associated with themselves
Transit Nodes
  Do not originate or terminate demand traffic, but switch it for other nodes
VoD example:
User Regions R0-R3
Data Centers DC0-DC2
Core Switches N0-N8
Which are access and which are transit?

## Slide 4: Node Type Caveats I
Management/Control Plane Traffic
  All nodes must, in some way, be involved with the management or control planes and hence transit nodes originate and terminate some traffic.
  In general demand traffic is much, much greater than management or control traffic. Why?
Additional Access Switching and/or De-multiplexing
  Access nodes may represent entire networks themselves with some internal nodes acting as transit nodes
  Even end systems perform de-multiplexing. Can you think of examples?

## Slide 5: Node Type Caveats II
Hybrid Nodes
  IXP’s with co-location services for CDNs
    Internet Exchange Points (https://en.wikipedia.org/wiki/Internet_exchange_point )
  Netflix co-locating at ISPs
    http://www.networkworld.com/community/blog/netflix-goes-edge-internet
Sometime node definitions depend on the “granularity” of our view.
  In network design we tend to start with coarser grained models and then refine them if warranted.

## Slide 6: Types of Expenses
Capital Expenses (CapEx)
  Costs to “build it”
    Installation and acquisition of infrastructure, cables, and equipment
    Examples: digging trenches, laying conduit, acquiring cables, laying cables, cable trays, equipment racks, switches, etc…
Operational Expense (OpEx)
  Costs to “run it”
    Power, network administrators, repair, maintenance, depreciation

## Slide 7: Link Placement Design IA
Problem
  Select links and their capacity to design a minimal OpEx network subject to a CapEx budget.
  Constants (link path based formulation)
    B upper bound for capital budget
    volume of demand d
    1 if link e is in demand path d,p; 0 otherwise
    unit maintenance cost (OpEx) of link e
    capital cost (CapEx) of link e
    upper bound for the capacity of link e. Note that even if this is extremely large we need it for our formulation.

## Slide 8: Link Placement Design IB
Givens
  List of candidate paths for each demand
Variables
  flow for demand d on its path p ()
  capacity of link e ()
  provisioning indicator 1 if used, 0 otherwise. Used in CapEx bounds and capacity bounds.

## Slide 9: Link Placement Design IC
Objective
  Minimize OpEx network costs
  Minimize:
CapEx budget Constraint
Demand satisfaction Constraints
  for

## Slide 10: Link Placement Design ID
Bandwidth Capacity Constraints
  for
“Can’t use it if its not installed” Constraint
  for
  What does this do?
  Remember that is 1 if the link is installed and zero otherwise.

## Slide 11: Example 1
Demands
  ('B14', 'B2'): 26.4, ('B5', 'B14'): 17.9, ('B5', 'B2'): 25.1, ('B5', 'B8'): 18.4, ('B8', 'B14'): 26.7

## Slide 12: Example 1 CapEx Visualization
(B7, B8): 264.97
(B4, B5): 265.38
(B0, B1): 313.45
(B5, B9): 338.68
(B6, B7): 364.00
(B3, B5): 465.24
(B3, B4): 488.41
(B2, B0): 538.91
(B2, B1): 636.99
(B10, B9): 667.89
(B12, B13): 765.40
(B12, B8): 776.49
(B11, B9): 888.73
(B10, B11): 973.48
(B4, B9): 1047.85
(B14, B13): 1171.28
(B5, B11): 1215.30
(B3, B1): 1224.42
(B3, B7): 1430.13
(B2, B3): 1507.64
(B8, B13): 1546.46
(B8, B13): 1546.46
(B14, B12): 1726.92
(B6, B8): 2042.67
(B6, B0): 2066.16
(B4, B8): 2273.53
(B14, B10): 2371.38
(B10, B13): 3058.32
CapEx based on length and a random multiplying integer
  CapEx shown as width of dashed lines

## Slide 13: Example 1: Results A
With a CapEx bound of 18,566.66
Optimum OpEx value of 50,116.57

## Slide 14: Example 1: Results B
With a CapEx bound of 12,068.33 (lower)
Optimum OpEx value of 50,448.92 (bigger)

## Slide 15: Example 1: Results C
With a CapEx bound of 11,140.00 (lower)
Optimum OpEx value of 51,250.81 (bigger)

## Slide 16: Example 1: Results D
With a CapEx bound of 9,283.33 (lower)
Optimum OpEx value of 64,375.67 (bigger)

## Slide 17: Optimizing both CapEx and OpEx
What if we…
  Want to optimize on CapEx?
  Optimize on a combination of CapEx and OpEx
  Find the minimum CapEx to produce a viable network?
Can we reuse some of what we have?

## Slide 18: Optimizing CapEx and OpEx
Constants (link path based formulation)
  B upper bound for capital budget
  volume of demand d
  1 if link e is in demand path d,p; 0 otherwise
  unit maintenance cost (OpEx) of link e
  capital cost (CapEx) of link e
  upper bound for the capacity of link e. Note that even if this is extremely large we need it for our formulation.

## Slide 19: Optimizing CapEx and OpEx
Variables
  flow for demand d on its path p ()
  capacity of link e ()
  provisioning indicator 1 if used, 0 otherwise. Used in CapEx bounds and capacity bounds.

## Slide 20: Optimizing CapEx and OpEx
Objective
  Minimize OpEx network costs
  Minimize:
CapEx budget Constraint
Demand satisfaction Constraints
  for

## Slide 21: Optimizing CapEx and OpEx
Bandwidth Capacity Constraints
  for
“Can’t use it if its not installed” Constraint
  for
  What does this do?
  Remember that is 1 if the link is installed and zero otherwise.

## Slide 22: Example
Result from minimization with previous CapEx values and OpEx values scalled down by 0.01
  Objective value = 9,283.33, used this as a basis for the CapEx bounds in the previous formulation examples.